## Slide 1: Badger Remote Mouse
Yuye Wang, Xiufeng Xie, Chun Wang, Jack Chiu
11/12/2012

## Slide 2: Agenda
Motivation
System Implementation
Challenges & Limitations
Summary
Our Application vs. Related Work
User Interface

## Slide 3: Motivation

## Slide 4: Motivation: 3D Mouse
Touchpads in notebook is not easy to use
Always bringing mouse is not convenient.
Traditional mouse needs a solid surface

## Slide 5: Motivation: Leg Control While Typing
Switch between keyboard and mouse
Keyboard typing takes both of your hands

## Slide 6: Motivation: Always at Hand
People will carry their phones all the time

## Slide 7: Motivation: Help disabled people
Also for people with hand disability
They can use their leg to control a PC

## Slide 8: Our Application vs. Related Work

## Slide 9: Related Work (i)
There are many remote mouse application
Most of them are for Android Phone/iPhone

## Slide 10: Related Work (ii)
Not so many for Windows Phone
Most are simply touchpad
  Use touch screen on the phone as the touch pad

## Slide 11: Our Work: Not Only A Touch Pad
Use the reading of the accelerometer and gyroscope on the phone to control mouse cursor
No need to use your finger

## Slide 12: Our Work: Release Your Hand
Keep on typing, use your leg to control the mouse cursor
Programmers will be
happy about this
when busy typing

## Slide 13: Our Work: Multiple Operation Modes
All in one
  Leg Control
  3D mouse
  PPT clicker
  2D mouse
  Touchpad

## Slide 14: Demo

## Slide 15: User Interface

## Slide 16: Server UI
Windows Form Application
  More friendly to normal users
Windows Console
  For debugging

## Slide 17: Client UI
Main panorama
Home
Settings
Modes
Five functions
Leg Control
Clicker
2D mouse
3D mouse
Touch pad
Help pivots

## Slide 18: Panorama Page

## Slide 19: Functions Page

## Slide 20: System Implementation

## Slide 21: Update Sensor Data
Update sensor data periodically
Accelerometer
X-axis
Y-axis
Z-axis
Attitude
Yaw angle
Pitch angle
Roll angle

## Slide 22: Prepare Data to Send
Pack sensor data and other control data (e.g. mouse button click control) into a data string
Header indicates operation mode
1: PPT clicker
2: 2D Mouse
3: 3D Mouse
4: Leg Control
5: Touch Pad

## Slide 23: Send Data: How to send?
Send control data to the laptop (server)
  Wi-Fi socket (UWNet will block our application)
  TCP/IP
Set up your laptop as a virtual AP
  Open “cmd” in administrator mode
  Enter (example): netsh wlan set hostednetwork mode=allow ssid=xxf key=12345678
  Enter: netsh wlan start hostednetwork
Shut down the virtual AP
  Enter: netsh wlan stop hostednetwork

## Slide 24: Send Data: When to send?
Send control data periodically?
Problem:
  The application always crashes with the exception:
    "An existing connection was forcibly closed by the remote host socket“
Why: Real-time application vs. Windows
  If the server cannot deal with old data before new data come, the thread will be blocked, then the application crashes.

## Slide 25: Send Data: Less Burden?
Transmit less data to server
  Less digits for sensor data
  Increase interval between transmissions
  Each operation mode only transmit necessary data for its own functionality
Larger buffer in server side

## Slide 26: Send Data: Use Feedback
Press “Start”
Unpredictable Processing Delay
Control Data
Feedback
Receiving Feedback
        Windows is not a real-time system

## Slide 27: Send Data: Feedback Triggered
The sending frequency of control data will never exceed the processing ability of the server
Advantage
  More stable
  More fluent:
    no need to be conservative for the worst case processing time

## Slide 28: Laptop receive data from WP
Extract control parameters from received data string
  Operation Mode
  Accelerometer: X, Y, Z
  Attitude: Yaw, Pitch, Roll
  Mouse click indicator

## Slide 29: Mode Selection
Server side program will figure out the operation mode base on the header of received data string.
  1: PPT clicker
  2: 2D Mouse
  3: 3D Mouse
  4: Leg Control
  5: Touchpad

## Slide 30: Smooth received sensor data
First order low pass filter
Ripple in sensor data:
  unconscious movement

## Slide 31: Sensor data cursor location
Mathematic model
  Cursor location is (x,y)
  x: location of cursor in the x-axis of the screen
  y: location of cursor in the x-axis of the screen
  Roll: smartphone rotation angle
  Pitch: smartphone pitch angle

## Slide 32: Linear Mapping Algorithm
  X axis: use the rotation of the phone
  Y axis: use the pitch up and down
  are predetermined parameter

## Slide 33: Design Mapping Parameters
Screen

## Slide 34: Learning Algorithm
Problem
  Users have different
  bodies & habits
  The range of sensor
  reading will be different
Solution
  Learning algorithm
  Gather user data in the training phase
  Use learnt data to update mapping parameters

## Slide 35: Set mouse cursor to the position
Easy to implement using windows API
Import “user32.dill”
  Get cursor position
  Set cursor position
  Mouse Events
    Mouse button up & down
    Mouse wheel

## Slide 36: Simulate Mouse Button Click
Leg control
  Set a threshold for acceleration
    If acceleration on Z-axis (up/down) exceeds the threshold, perform left button click
    If acceleration on X-axis (left/right) exceeds the threshold, perform right button click
  Do not interfere with cursor position control, as long as you do it slow enough

## Slide 37: Simulate Mouse Button Click
2D/3D mouse
  Display mouse button on the touch screen of windows phone
    Use “Tap” Event rather than “Click” Event
    Double Tap
  Pack mouse button click variable in the data string transmitted to the laptop
  Laptop perform mouse click based on the received mouse button click variable.

## Slide 38: Send feedback to smartphone
Transmit a data string back to the phone
  In normal case, transmit “connected”
  If mouse button is successfully clicked, transmit “clicked”
clicked

## Slide 39: Phone gives feedback to user
After receiving the "clicked" signal from the server, WP will vibrate as a feedback that the button is successfully clicked.
On receiving the feedback, WP will send current sensor data and other control data to the server

## Slide 40: System Diagram
Client Socket
Server Socket
Data String
Feedback
Sensors
UI
Sensor Data
Control Data
Extract Data
UI
Start/Pause
Mode Selection
LPF
Learning Algorithm
Mapping Algorithm
Control Position
Control Click

## Slide 41: Challenges & Limitations

## Slide 42: Selection of Click Threshold
Problem
  Simulate mouse button click without interfering with cursor position control
  Use acceleration on different axis to control click
    Threshold to large: difficult to trigger click
    Threshold to small: always interfere with position control

## Slide 43: Feedback to User
Problem
  Users want feed back
  Physical button feedback:
    Feeling on the hand
    Click sound
  No physical button in our application
Solution
  Vibration after click
    After a mouse button click, server sends a "clicked" signal back to WP.
    After receiving the "clicked" signal, WP will vibrate.

## Slide 44: Smooth Data
Problem
  You thigh is not a stable platform
  Sensor reading will ripple
Solution
  A first order low pass filter is used to smooth sensor data
  Eliminate the rippled caused by the inadvertent movement of users.

## Slide 45: What is the proper place
Method | Phone location | User status | User behavior | Easy to use?
Hand control | At hand | No limit | Rotate phone with hand | Good
Thigh control | Tied above thigh | Sitting | Move thigh | Good
Ankle control | Tied above ankle | Sitting | Move ankle | Fair
Body control | Tied above ankle | Standing | Move body | Fair

## Slide 46: Precision of the sensor
Sensors equipped on Windows Phone are not precise enough.
Use integration of acceleration, we cannot get current velocity of the phone.
Fatal for 2D mouse

## Slide 47: Take away

## Slide 48: Take away
Fast
Simple
User friendly
Integration

## Slide 49: Summary

## Slide 50: Thank you!